## Slide 1: CISN ShakeMap Improvements since 2012
NC/SC Products delivered to USGS (USGS website, ShakeCast, PAGER) through new Product Distribution Layer (PDL)
ShakeMap links for SC, NC and CGS at http://www.cisn.org
Hardware upgrades at SC/CGS
Configurations shared between operations centers (NC, SC, CGS)
Notes: For SC: only 2012; 22 events without ShakeMap (not shown) – events may have been cancelled or magnitude downgraded; 4 maps with times > 10 minutes for most of them, ShakeMap had to be run by hand
For NC: 9 with T>10 min, 7 with T>15 min. Latter: magnitude raised when moment tensor done or relocated closer to border of network.
CGS: only started delivering to PDL in May; “delayed” because they wait for location/magnitude from authoritative network

## Slide 2: CISN ShakeMap Performance 2012-2013
Notes: For SC: only 2012; 22 events without ShakeMap (not shown) – events may have been cancelled or magnitude downgraded; 4 maps with times > 10 minutes for most of them, ShakeMap had to be run by hand
For NC: 9 with T>10 min, 7 with T>15 min. Latter: magnitude raised when moment tensor done or relocated closer to border of network.
CGS: only started delivering to PDL in May; “delayed” because they wait for location/magnitude from authoritative network

## Slide 3: CISN ShakeMap Redundancy and Backup
Configurations shared between operations centers
ShakeMaps published rapidly to http://www.cisn.org/shakemap/ and http://earthquake.usgs.gov/earthquakes/shakemap/
CGS to publish backup ShakeMap after 10 minutes if no SC/NC ShakeMap
CGS has its own SM data
CGS receives event info through EIDS/PDL
CGS has other real-time responsibilities
Notes: For SC: only 2012; 22 events without ShakeMap (not shown) – events may have been cancelled or magnitude downgraded; 4 maps with times > 10 minutes for most of them, ShakeMap had to be run by hand
For NC: 9 with T>10 min, 7 with T>15 min. Latter: magnitude raised when moment tensor done or relocated closer to border of network.
CGS: only started delivering to PDL in May; “delayed” because they wait for location/magnitude from authoritative network